## Slide 1: FEC and Registers
Prep Check
xx
LO: To understand the role of each register in the FEC

## Slide 2: FEC and Registers
Specification Point
3.7.3.2 The fetch–execute cycle and the role of registers within it
LO: To understand the role of each register in the FEC

## Slide 3: FEC and Registers
Question
A computer system has a clock speed of 3 GHz, a 32 bit data bus and a 24 bit address bus. What would be the precise effect of:
(i) increasing the clock speed to 6 GHz?
(ii) increasing the size of the data bus to 64 bits?
(iii) increasing the width of the address bus to 40 bits?
LO: To understand the role of each register in the FEC

## Slide 4: FEC and Registers
Answer
(i) Halve the time to perform an instruction;
  Acceptable, Instructions performed more quickly.
(ii)Increase the number of bits transferred at any one time from 16 to 32. Or, double the number of bits transferred at any one time.
(iii) Increase the number of memory addresses (1st mark), from 224 to 240 (2nd mark)
LO: To understand the role of each register in the FEC

## Slide 5: FEC and Registers
Structure of the Processor
Program control unit
  Fetches program instructions from memory , decodes them and executes them one at a time.
Arithmetic and logic unit
  ALU performs arithmetic and logical operations
Registers
  Fast memory locations inside the CPU (Or I/O controller), can be dedicated or general purpose.
LO: To understand the role of each register in the FEC

## Slide 6: FEC and Registers
Structure of the Processor
Internal clock
  Derived from the system clock
Internal buses
  Link the control unit , ALU and the registers
Logic gates
  Used for flow control
LO: To understand the role of each register in the FEC

## Slide 7: FEC and Registers
Registers
The control unit needs somewhere to store details of the operations being dealt with by the fetch–execute cycle.
The ALU needs somewhere to put the results of any operations it carries out.
There are a number of storage locations within the processor that are used to store this sort of data.
They are called registers and although they have a very limited storage capacity they play a vital role in the operation of the computer.
LO: To understand the role of each register in the FEC

## Slide 8: FEC and Registers
Common Registers
The Current Instruction Register (CIR) stores the instruction that is currently being executed by the processor.
The Program Counter (PC) stores the memory location of the next instruction that will be needed by the processor.
Each time an instruction is fetched, the value held in the PC is incremented.
LO: To understand the role of each register in the FEC

## Slide 9: FEC and Registers
Common Registers
The Memory Buffer Register (MBR) also known as the Memory Data Register (MDR) holds the data that has just been read from or is about to be written to main memory.
The Memory Address Register (MAR) stores the memory location where data in the MBR is about to be written to or read from.
LO: To understand the role of each register in the FEC

## Slide 10: FEC and Registers
Status Register
The status register keeps track of the status of various parts of the computer – for example, if an overflow error has occurred during an arithmetic operation.
Holds Condition Codes
A ‘flag’ to represent where the outcome of an operation is:
        Positive
        Negative
        Overflow
        Zero
LO: To understand the role of each register in the FEC

## Slide 11: FEC and Registers
Interrupt register
The interrupt register is a type of status register. It stores details of any signals that have been received by the processor from other components attached to it, for example, the I/O controller for the printer.
LO: To understand the role of each register in the FEC

## Slide 12: FEC and Registers
Dedicated registers
  Stack pointer (SP)
  Program Counter (PC)
  Status register (SR)
  Accumulator (ACC)
  Current instruction register (CIR)
  Memory address register (MAR)
  Memory buffer register (MBR)
LO: To understand the role of each register in the FEC

## Slide 13: FEC and Registers
  0101 0000 0000 0111
Machine Code instructions
LO: To understand the role of each register in the FEC
Op-Code
Operand
Current Instruction in Machine Code

## Slide 14: FEC and Registers
Fetch-Execute Cycle Animation
LO: To understand the role of each register in the FEC

## Slide 15
0000 0000 0000 0100
Instruction Decoder
ALU
1
2
3 0101 0000 0000 0110
4
5
6
0000 0000 0000 0011
Current Instruction Register (CIR)
Memory Address Register
Memory Buffer Register
Main Memory
Address Bus
Data Bus
:
+1
Program Counter
Accumulator
Op-code
Operand
“ADD #6”
0000 0000 0000 0011
Fetch
MAR  [PC]
PC  [PC] + 1
MBR  memory contents
CIR  [MBR]
0101 0000 0000 0110
0000 0000 0000 0100
0000 0000 0110
0101
The Fetch-Execute cycle

## Slide 16
0000 0000 0000 0100
Instruction Decoder
ALU
1
2
3 0101 0000 0000 0110
4
5
6
0000 0000 0000 0011
Current Instruction Register (CIR)
Memory Address Register
Memory Buffer Register
Main Memory
Address Bus
Data Bus
:
+1
Program Counter
Accumulator
Op-code
Operand
“ADD #6”
0000 0000 0000 0011
Execute
Decode instruction
Execute instruction
0101 0000 0000 0110
0000 0000 0000 0100
0000 0000 0110
0101
0000 0000 0000 0011
0000 0000 0110
0000 0000 0000 0100
0000 0000 0000 1010
6 + 4
= 10
“ADD operand to accumulator”
+
End of F-E Cycle
0101
The Fetch-Execute cycle

## Slide 17: FEC and Registers
Register Transfer Notation
MAR  [PC]
PC  [PC] +1; MBR  [Memory]
CIR  [MBR]
[CIR] decoded and executed
LO: To understand the role of each register in the FEC

## Slide 18: FEC and Registers
Describing the FEC Process
LO: To understand the role of each register in the FEC
1 | Contents of Program Counter transferred to MAR
2 | Program Counter incremented; Contents of memory address in MAR transferred to MBR
3 | Contents of MBR transferred to the CIR
4 | [CIR] decoded and executed

## Slide 19: FEC and Registers
FEC additional points
Fetch:
Some instructions need to load a number of bytes or words, so they may need to be fetched as successive parts of a single instruction.
LO: To understand the role of each register in the FEC

## Slide 20: FEC and Registers
FEC additional points
Execute:
Instruction sets are either classed as an RISC (reduced instruction set) or a CISC (complex instruction set).
An instruction set is a library of all the things the processor can be asked to do. Each instruction in the instruction set is accompanied by details of what the processor should do when it receives that particular instruction. This might be to send the contents of the MBR to the ALU.
RISC and CISC instruction sets
LO:

## Slide 21: FEC and Registers
Prep
Complete the exam questions on Copia
LO: To understand the role of each register in the FEC

## Slide 22
Key words:
Noted clearly
Topic specific vocabulary wherever necessary
Icon for extension activity if appropriate
You might want to develop subject specific icons
Icon same colour as dept ex book