## Slide 1: Boolean Algebra
Half Adder
The ‘Half Adder’ circuit performs addition of two binary values
Output S stands for Sum
Output C stand for Carry
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 2: Boolean Algebra
Full Adder
The ‘Full Adder’ circuit performs addition of more than two binary values
Full adder allows for the carry bit from the first addition to be used in the addition of the next two bits
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 3: Boolean Algebra
Edge-triggered D type flip-flop
Logic gates and logic circuits show how 0s and 1s can be manipulated to evaluate Boolean expressions.
Data is passed around these gates and circuits at very high speed.
However, as soon as the next set of inputs are fed in, the previous inputs are lost.
Often the next set of inputs come from the outputs of the previous calculation.
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 4: Boolean Algebra
Edge-triggered D type flip-flop
Therefore some form of memory is needed and this is provided by a flip-flop, which is capable of storing one bit.
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 5: Boolean Algebra
Simplifying Boolean Expressions
When using Boolean expressions it is good practice to reduce the expression into its simplest form.
As Boolean algebra is used to create logic gates, simplifying the expressions also simplifies the actual circuit that will be built.
An expression may be made up of many variables, usually referenced as letters (A,B,C, etc.) each of which can produce a result of 0 or 1.
This can lead to the creation of complex Boolean expressions.
Therefore rules have been developed as a method of simplifying expressions.
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 6: Boolean Algebra
Simplifying Boolean Expressions - Rules
LO: To understand the rules of Boolean algebra and De Morgan’s Law
A.B = B.A | The order in which two variables are ANDed makes no difference
A+B = B+A | The order in which two variables are ORed makes no difference
A.0 = 0 | A variable ANDed with 0 equals 0
A+1 = 1 | A variable ORed with 1 equals 1
A+0 = A | A variable ORed with 0 equals the variable
A.1 = A | A variable ANDed with 1 equals the variable
A.A = A | A variable ANDed with itself equals the variable
A+A = A | A variable ORed with itself equals the variable
A.Ā = 0 | A variable ANDed with its inverse equals 0

## Slide 7: Boolean Algebra
Homework
Draw truth tables to demonstrate that each of the rules on the previous slide are correct e.g.
A.0 = 0 A.1 = A
LO: To understand the rules of Boolean algebra and De Morgan’s Law
A | 0 | X
0 | 0 | 0
1 | 0 | 0
A | 1 | X
0 | 1 | 0
1 | 1 | 1

## Slide 8: Boolean Algebra
Review of prep – Rules for Boolean Expressions
LO: To understand the rules of Boolean algebra and De Morgan’s Law
A.B = B.A | The order in which two variables are ANDed makes no difference
A+B = B+A | The order in which two variables are ORed makes no difference
A.0 = 0 | A variable ANDed with 0 equals 0
A+1 = 1 | A variable ORed with 1 equals 1
A+0 = A | A variable ORed with 0 equals the variable
A.1 = A | A variable ANDed with 1 equals the variable
A.A = A | A variable ANDed with itself equals the variable
A+A = A | A variable ORed with itself equals the variable
A.Ā = 0 | A variable ANDed with its inverse equals 0

## Slide 9: Boolean Algebra
Simplifying Boolean Expressions – More Rules
LO: To understand the rules of Boolean algebra and De Morgan’s Law
A+ Ā = 1 | A variable ORed with its inverse equals 1
Ā = A | A variable that is double inversed equals the variable
(A.B).C = A.(B.C) | It makes no difference how the variable are grouped together when ANDed
(A+B)+C = A+(B+C) | It makes no difference how the variable are grouped together when ORed
A.(B + C) = A.B + A.C | The expression can be distributed or factored out meaning that variables can be moved in and out of brackets either side of the expression. In English this expression would be A AND (B OR C) = (A AND B) OR (A AND C ).

## Slide 10: Boolean Algebra
De Morgan’s Law
De Morgan’s Law is a another way of simplifying Boolean statements.
Invert all the variables, changing ANDs to OR and ORs to ANDs.
Then invert the whole expression.
One application is to simplify statements so that only NAND or NOR gates are used when building circuits.
The basic principles are:
  Rule 1: NOT (A AND B) is the same as (NOT A) OR (NOT B)
  Rule 2: NOT (A OR B) is the same as (NOT A) AND (NOT B)
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 11: Boolean Algebra
De Morgan’s Law
LO: To understand the rules of Boolean algebra and De Morgan’s Law
A + B = A . B
A . B = A + B

## Slide 12: Boolean Algebra
De Morgan’s Law
Draw a truth table to prove this law is correct
LO: To understand the rules of Boolean algebra and De Morgan’s Law
A + B = A . B
A . B = A + B

## Slide 13: Boolean Algebra
Homework
LO: To understand the rules of Boolean algebra and De Morgan’s Law

## Slide 14
Key words:
Noted clearly
Topic specific vocabulary wherever necessary
Icon for extension activity if appropriate
You might want to develop subject specific icons
Icon same colour as dept ex book