## Slide 1: Errors in binary fractional numbers
LO: To understand what errors can occur when dealing with numbers with a fractional part
To be able to identify each type of error will occur and be able to calculate absolute and relative errors
To be understand when a rounding error might occur
To be able to identify a normalised floating point binary number and explain why normalising the number is important

## Slide 2: Errors in binary fractional numbers
Specification Points
3.5.4.7 Range and precision (A level only)
3.5.4.8 Normalisation and floating point form (A level only)
3.5.4.9 Underflow and overflow (A level only)
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 3: Errors in binary fractional numbers
Underflow and Overflow
It is possible when using signed binary that you will generate a number that is either too large or too small to be represented by the number of bits that are available to store it.
When the number is too large, we get an overflow and when it is too small we get an underflow.
An example of overflow is if 00000001 (1 in decimal) was added to 01111111 (127 in decimal), it would generate the answer 1000000 (128 in decimal).
However, using two’s complement, we would actually get the answer -128.
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 4: Errors in binary fractional numbers
Underflow and Overflow
It is possible when using signed binary that you will generate a number that is either too large or too small to be represented by the number of bits that are available to store it.
When the number is too large, we get an overflow and when it is too small we get an underflow.
An example of overflow is if 00000001 (1 in decimal) was added to 01111111 (127 in decimal), it would generate the answer 1000000 (128 in decimal).
However, using two’s complement, we would actually get the answer -128.
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 5: Errors in binary fractional numbers
Underflow
LO: To understand what errors can occur when dealing with numbers with a fractional part
-1 | ½ | ¼ | 1/8 | 1/16 | 1/32 | 1/64 | 1/128
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
-8 | 4 | 2 | 1
1 | 0 | 0 | 0
exponent
mantissa
= -15
-1 | ½ | ¼ | 1/8 | 1/16 | 1/32 | 1/64 | 1/128 | … | … | … | … | … | … | … | … | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
NOTE: Change slide to show a number that is too small to be represented using 8 bit mantissa and 4 bit exponent

## Slide 6: Errors in binary fractional numbers
Normalisation and Precision
Normalisation is a technique used to ensure that when numbers are represented they are as precise as possible in relation to how many bits are being used.
The exponent is used to ensure that the floating point is placed to optimise the precision of the number. Eg:
234000 can be represented as:
23 400 × 101
2.34 × 105
0.00000234 × 1011
The second option is the best way to represent the number as it uses the least number of digits, yet provides a precise result.
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 7: Errors in binary fractional numbers
Normalised Binary Numbers
With binary codes, normalisation is equally important.
In order to be normalised the first bit of the mantissa, after the binary point, should always be a 1 for positive numbers, or a 0 for negative numbers and the bit before the binary point should be the opposite.
So a normalised positive floating point number must start 0.1 and a normalised negative floating point number must start 1.0.
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 8: Errors in binary fractional numbers
LO: To understand what errors can occur when dealing with numbers with a fractional part
Notes: https://www.youtube.com/watch?v=XUauMgQf-1w

## Slide 9: Errors in binary fractional numbers
Normalised or not? Positive or negative?
LO: To understand what errors can occur when dealing with numbers with a fractional part
00110010 0011
01000000 0010
01000000 0010
10000100 0110
11100000 0010
10110000 0010

## Slide 10: Errors in binary fractional numbers
Rounding Errors
When working with decimal numbers, we will get rounding errors. For example, 1/3 in decimal is 0.3 recurring.
We are comfortable with using 0.33 or perhaps 0.333 to represent 1/3.
Obviously there is a degree of error in this calculation. Whether it is acceptable or not depends on what our program was doing.
A similar phenomenon occurs with binary representation. For example, if you try to make 0.1 into binary you will find that you get a recurring number, so it is not possible to exactly represent it.
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 11: Errors in binary fractional numbers
LO: To understand what errors can occur when dealing with numbers with a fractional part
Rounding Errors
Notes: https://www.youtube.com/watch?v=PZRI1IfStY0

## Slide 12: Errors in binary fractional numbers
Absolute and Relative Errors
The absolute error is the actual mathematical difference between the answer and the approximation of it that you can store.
3.789 – 3.75 = 0.039
Absolute error is 0.039
LO: To understand what errors can occur when dealing with numbers with a fractional part
Number you wanted to store / represent
Closest representation in binary

## Slide 13: Errors in binary fractional numbers
Absolute and Relative Errors
For example, if a calculation required 8 decimal places, but we only allocated 8 digits, we would have to either round or truncate the number.
So the number 1.65746552 would become 1.6574655.
In this case to work out the absolute error we would subtract the two values and that would give us an absolute error of 0.00000003.
Note that the absolute error is always a positive number.
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 14: Errors in binary fractional numbers
Relative Errors
Relative error looks at the value that was being stored and then decides on a relative margin of error. This is represented as a percentage.
In this way you are comparing the actual result to the expected result.
Relative error = Absolute error
Number intended to be stored
LO: To understand what errors can occur when dealing with numbers with a fractional part

## Slide 15
Key words:
Noted clearly
Topic specific vocabulary wherever necessary
Icon for extension activity if appropriate
You might want to develop subject specific icons
Icon same colour as dept ex book